## Slide 1
Object state between contacts
01
Second-week research report
What does current shape reveal,
and what does interaction history add?
Spatial 2D contact with fast and slow internal relaxation
The current shape carries substantial information.
Contact and recovery history reduce the remaining prediction error.
28 October 2026
Notes: 这周我把上次的一维接触扩展成了真正的空间二维模型。研究主题仍然是物体隐藏状态，而不是材料本构本身。本轮集中回答两个问题：当前侧向形变已经告诉了我们多少信息，以及历史的价值来自多长时间，还是来自其中的接触与恢复过程。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/RESULTS.md
Reference design: 10_1.pdf, 12 pages, Arial, 1600 x 900 px equivalent. Source PDF is retained unchanged.

## Slide 2
What changed since the first report
02
First report | This week
1D motion with two internal variables | Spatial 2D FEM with lateral deformation
History predicts different future responses | Separate current shape from additional history
A short classical observer can already work well | Separate waiting time from informative contact data
Shared feedback gave little extra action benefit | Keep action benefit as a separate, unfinished test
The meeting feedback motivated the 2D contact and lateral-response test.
The 2D-to-3D and lateral-response feedback comes from the recorded meeting recap.
Notes: 上周的三个判断保留：历史能帮助预测，状态可以用于不同未来控制，但共同反馈下的动作收益很小。经典估计器也已经很强。这周没有假设长历史或者神经网络必须获胜，而是把空间形变和传感信息加进去。关于老师反馈，2D到3D和侧向变化来自会后中文录音复述，现场英文片段只支持回到网格图和单指例子，不能说老师指定了某个算法。
Sources (relative to the repository):
1D/RESULTS.md
1D/PRESENTATION_MAP.md
2D/runs/information/channels_contact_20261026/RESULTS.md
Meeting source: D:/capp/NR/Documents/Codex/2026-10-23-project-feedback/项目反馈总结与转录.md (A 00:00.5-00:06; C 00:08-00:15.8).

## Slide 3
A spatial body produces the force and lateral response
Fixed bottom, free sides, one round rigid indenter. The deformation comes from the FEM solution.
03
Recorded 2D pilot. Synthetic material. Quasistatic body with a dynamic tool. Deformation shown at 1x scale.
Notes: 先看物理过程。底边固定，侧边自由，压头加载、保持、释放、等待，再接触。右侧分别记录实际接触力、命令与实际运动、两侧标记点。脱离接触后力回到零，但侧向形变仍在恢复。这里沿用已经验证过的空间2D演示图，后面统计来自新的24条历史。材料参数是合成参数，物体采用准静态平衡，压头保留动力学，尚未做真实材料标定。
Sources (relative to the repository):
2D/runs/2d_contact/pilot_c9dd23016896/figures/01_spatial_process.json
2D/runs/information/channels_contact_20261026/physics.json
2D/src/nr2d/physics.py

## Slide 4
The physical state contains more than the current measurement
04
Physical state
Fast and slow internal strain fields
Tool position and velocity
Relaxation times: 0.12 s and 0.90 s
Equilibrium determines deformation and contact.
Available observation
Tool position, velocity and total force
Optional left/right lateral displacement
During detached waiting, force is zero.
Lateral shape still changes during recovery.
Classical state estimate
Fit six nonnegative coefficients for the two internal fields.
Propagate the estimate with the same FEM and a future command.
The estimate is a restricted physical representation. Current shape alone is not a sufficiency proof.
Notes: 完整状态包括快慢内部应变场和压头位置速度。在已知参数的模型中，这些状态足以向前推进。机器人获得的瞬时测量只是位置、速度、总力和可选的两侧位移。我们用同一个经典观察器，在三个弹性基底上拟合快慢两个场，共六个非负系数。它是完整内部场的近似。当前形变很有信息，但还不能直接把它等同于对未来充分的状态。
Sources (relative to the repository):
2D/src/nr2d/estimators.py
2D/runs/information/channels_contact_20261026/physics.json
2D/runs/information/channels_contact_20261026/test/test_5000/repeat_0/result.json

## Slide 5
The comparison changes only the available information
Same physical histories, prediction time, future solver and observed noise draw.
05
Information | Motion + force | Motion + force + lateral shape
Current sample | Position, velocity, total force | The same sample plus two lateral markers
Recent history | The same channels over 0.2 or 0.8 s | The same window plus lateral history
24 independent loading histories
Three noise draws per history.
History, rather than noise draw, is the statistical unit.
Three separate calibration histories
Equal tuning budgets select one shared preset.
Estimate once, then predict Slow and Fast press.
Prediction starts at 1.40 s. Disabled channels are absent from both initialization and fitting.
Notes: 所有方法使用相同的物理历史和同一份噪声观测，只屏蔽通道，关闭侧向后它不能继续用于初始化或拟合。三条校准历史选超参数，24条新测试历史各有三次独立噪声。统计单位是完整历史，不能把72次噪声重复当72个独立物体。同一状态估计直接用于慢压和快压，快压不参与调参。真实内部场和已知松弛初态的完整重放只作为特权参考。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/study.json
2D/runs/information/channels_contact_20261026/calibration.json
2D/runs/information/channels_contact_20261026/verification/data_contract.json
2D/tests/test_observer_config.py

## Slide 6
The same future command exposes different prediction errors
First prespecified test history, noise draw 0, Slow press. History conditions use the recent 0.8 s.
06
Current motion + force
Current + lateral shape
0.8 s motion + force
0.8 s + lateral shape
True response
Contact force (mN)
Prediction error (mN)
Chart: 
Chart: 
Time after prediction start (s)
Time after prediction start (s)
All predictions start from the same observed tool state. Future achieved motion is not supplied to the estimator.
Notes: 左图是同一慢压命令下的力曲线，右图把预测减去真实响应。当前运动和总力最容易失去恢复信息，加上侧向形变后已经明显改善。0.8秒历史进一步靠近真实曲线。这个例子固定取测试编号5000的第一次噪声，不按未来误差挑选。总体结论要看后面的24条完整历史。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/test/test_5000/repeat_0/curves.npz
2D/runs/information/channels_contact_20261026/figures/01_information_curves.json

## Slide 7
Current lateral shape carries substantial predictive information
Force RMSE for Slow press, averaged within history and then across 24 histories.
07
Chart: 
| Current motion + force | Current + lateral shape
Force RMSE | 11.5035 | 2.1982
Force RMSE (mN)
9.31 mN
paired reduction in error
95% interval: 7.06 to 11.57 mN
Shape exposes recovery
while contact force is zero.
Both lateral markers share one underlying mode in this symmetric model. Their measurement noise is independent.
Notes: 24条历史上，只有当前运动和力的误差是11.50毫牛，加上当前侧向形变后降到2.20毫牛。配对改善9.31毫牛，按完整历史bootstrap的95%区间是7.06到11.57。它说明当前侧向信息不能忽略。不过对称模型的左右标记实际上反映同一个形变模式，不能把两个标记当成两个独立物理自由度。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/metrics.csv
Intervals: 2,000 whole-history bootstrap resamples, pointwise exploratory 95% intervals.

## Slide 8
The recent 0.2 s contains waiting, while earlier data contain contact
Example history: load to 0.36 s, hold to 0.84 s, release to 1.10 s, wait to 1.40 s.
08
Observed contact force (mN)
Chart: 
Contact threshold | 4.5 | 4.5
Estimator input | Observation update | Propagation | Contact duration
Recent wait | 1.20-1.40 s | None | 0 s
Recent 0.8 s | 0.60-1.40 s | None | 0.32 s
Earlier contact | 0.72-0.92 s | 0.92-1.40 s | 0.20 s
Contact selection uses observed force > 4.5 mN and scans prior force. The contact method spans 0.68 s of motion here.
Notes: 这是本轮最重要的设计修正。最后0.2秒全是脱离接触后的等待，不能和一维里的接触窗口直接作同条件解释。我们另外找更早的连续0.2秒接触片段，仅由观测力超过4.5毫牛识别，拟合后用实际运动记录传播到当前。以这条历史为例，0.72到0.92秒更新，再传播0.48秒，总运动跨度0.68秒。选择片段还扫描了之前的力，因此不能叫只使用0.2秒历史。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/coverage.json
2D/runs/information/channels_contact_20261026/histories/test_5000.npz
2D/runs/information/channels_contact_20261026/test/test_5000/repeat_0/curves.npz

## Slide 9
History helps when it includes informative observations
Mean Slow-press force RMSE. The nominal-noise result uses all 24 independent histories.
09
Recent window
Earlier contact plus propagation
Chart: 
| 0 | 0.2 | 0.8
Without lateral | 11.5035 | 12.753 | 0.31382
With lateral | 2.1982 | 1.2864 | 0.23041
Force RMSE (mN)
Window duration (s)
Without lateral
With lateral
Channels | Recent wait | Earlier contact
Without lateral | 12.75 mN | 0.48 mN
With lateral | 1.29 mN | 0.39 mN
Current lateral: 2.20 mN
Recent lateral wait: 1.29 mN
Recent 0.8 s with lateral: 0.23 mN
Recovery dynamics and noise averaging both may help. Contact and duration are not completely disentangled.
Notes: 只看力的等待窗口没有有效更新，误差仍然很大。加入侧向后，0.2秒等待也有增益，说明恢复过程有信息，同时重复测量降噪也可能贡献。0.8秒包含接触，误差降到0.23毫牛。更早的接触片段再传播，也明显优于近期等待。我们还不能把全部改善都归因于接触，因为它使用了更长运动跨度。新批次里带侧向短历史的改善，也限制了旧8条测试中“噪声使短窗变差”的适用范围。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/RESULTS.md
2D/runs/information/channels_contact_20261026/coverage.json
2D/runs/2d_contact/pilot_c9dd23016896/RESULTS.md

## Slide 10
The same estimate also predicts a faster press
No refitting on the future action. Slow press alone selects the calibration preset.
10
Information used | Slow press | Fast press
Current + lateral shape | 2.20 | 2.52
Recent 0.2 s + lateral shape | 1.29 | 1.26
Earlier contact + propagation, with lateral | 0.39 | 0.42
Recent 0.8 s + lateral shape | 0.23 | 0.21
The estimate transfers across these two future commands.
Units: mN force RMSE. This is prediction reuse. The 2D study has not yet tested improvement in closed-loop actions.
Notes: 每次历史估计只做一次，慢压和快压使用完全相同的估计状态，运行记录用哈希核对过。快压没有参与校准。两种动作下的排序接近，0.8秒侧向历史的误差分别约0.23和0.21毫牛。这支持在这两种命令之间复用估计，但不能把它解释成跨任务普遍充分，也不能解释成闭环动作收益。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/verification/data_contract.json
Estimated-state hashes are identical across the two future branches.

## Slide 11
The classical observer is accurate, but repeated fitting is costly
11
Recorded result | What it changes
0.23 mN with the recent 0.8 s and lateral sensing | A neural model has no demonstrated accuracy gap to fill.
27.24 s median inference for that window | A recursive update should avoid refitting the same past.
201 of 576 fits reached the evaluation limit | Optimization status and update cost need separate checks.
All 72 force-only wait fits retained the initial coefficients | Waiting force cannot supply the missing state information.
The current estimate has no uncertainty and uses a restricted six-coefficient basis.
Timing is measured during an eight-worker CPU batch. Accurate simulation prediction does not imply real-time control.
Notes: 经典方法在接触数据足够时已经很准，所以这轮不能自然推出必须上RNN或JEPA。真正显露的问题是每次从头拟合很慢，0.8秒带侧向窗口在八进程批量下中位耗时27.24秒，而且没有不确定性。201次有限窗拟合触及七次函数评估上限。没有侧向的等待拟合全部停在初值附近，因此当前和短窗的误差差异还混合了先验放在哪个时刻、如何传播的影响，不能说历史本身有害。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/failures.json
2D/runs/information/channels_contact_20261026/RESULTS.md
2D/src/nr2d/estimators.py

## Slide 12
Next: retain the contact estimate through release and recovery
12
Immediate experiment
Compare recursive classical updates with the current window fits.
Measure prediction error, update time and uncertainty at several prediction times.
A small control to explain the history gain
Compare evolving recovery observations with repeated measurements of a fixed state.
This separates dynamic information from noise averaging.
Then test actions under common feedback
First check whether true-state information can help the selected task.
Full 3D robot simulation follows the 2D decision test, before real robot operation.
For discussion: which manipulation needs this state before feedback catches up, and which observable should define success?
Notes: 下一步先不换网络。用经典递推观察器把接触时估计到的状态带过释放与等待，在多个预测时刻比较误差、更新时间和不确定性。补一个静态重复测量对照，区分恢复动力学和降噪。之后做共同反馈动作实验，先确认真实状态参考在给定任务和动作条件下有潜在收益。如果连这个参考都没有收益，应改任务而不是继续改编码器。完整3D机械臂闭环仿真在实机之前。希望讨论的是：哪个操作确实需要反馈尚未来得及补齐的信息，以及应该用什么任务结果判定它有用。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/RESULTS.md#next-experiment
research/robot_manipulation/
Planned only: recursive observer, uncertainty calibration, shared-feedback 2D actions, complete 3D robot simulation, hardware.

## Slide 13
Appendix: all recorded prediction errors
Force RMSE in mN. Twenty-four histories, three independent nominal-noise draws per history.
13
Information | Slow press | Fast press
Current motion + force | 11.504 | 12.764
Current + lateral | 2.198 | 2.516
Recent 0.2 s, without lateral | 12.753 | 14.323
Recent 0.2 s, with lateral | 1.286 | 1.256
Recent 0.8 s, without lateral | 0.314 | 0.317
Recent 0.8 s, with lateral | 0.230 | 0.207
Earlier contact + propagation, without lateral | 0.476 | 0.514
Earlier contact + propagation, with lateral | 0.389 | 0.415
Full replay from a known relaxed start [privileged] | 0.0065 | 0.0075
True internal fields and the same solver [privileged] | 0.000 | 0.000
The references supply privileged state or initialization. They are not absolute optimal-control bounds.
Notes: 这一页保留所有方法的完整均值，避免只展示有效的条件。已知松弛初态的完整重放和真实内部场使用额外信息。真实内部场误差为零来自使用同一个状态和同一个前向求解器，不代表现实物理误差为零，也不是所有控制策略的最优上界。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/metrics.csv

## Slide 14
Appendix: paired gains across complete loading histories
Positive values mean lower force prediction error for Slow press.
14
Add current lateral shape
Chart: 
| 8.8336355 | 17.297893 | 13.433184 | 4.4673041 | 12.423369 | 9.5722055 | 9.8690114 | -0.038856044 | 0.80852306 | 13.781941 | 3.522638 | 6.8453523 | 19.053939 | 14.326623 | 14.018747 | -0.16143372 | 13.310014 | 19.454444 | 7.8353156 | 5.4516546 | 1.2490055 | 11.672473 | 8.8118515 | 7.4896701
24 histories | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09
95% interval | 0 | 0
Mean | 0
9.31 mN
[7.06, 11.57]
Add 0.2 s lateral wait
Chart: 
| -1.1581864 | 0.80323766 | 1.2763668 | 2.199763 | 1.0274193 | 0.44547809 | -0.43476294 | 1.0428918 | 2.4127628 | 0.40790782 | 0.92803142 | 2.1981743 | 0.38665096 | 0.81686587 | 1.4746337 | 0.49908863 | 2.1860167 | 0.94345981 | 1.5925044 | 0.099429687 | 1.4891375 | 0.6091326 | 0.7013753 | -0.063723844
24 histories | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09
95% interval | 0 | 0
Mean | 0
0.91 mN
[0.57, 1.27]
Add 0.8 s lateral history
Chart: 
| 0.98589542 | 1.9181155 | 2.0190219 | 2.8875149 | 2.2292544 | 1.1749816 | 1.0537575 | 2.5831834 | 3.5612028 | 2.0287316 | 1.7989672 | 3.3165945 | 0.76046619 | 1.6504241 | 1.5814082 | 2.26377 | 3.2673515 | 1.4896182 | 2.6006016 | 1.0948974 | 2.2822191 | 1.9413945 | 1.3009086 | 1.4360709
24 histories | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09
95% interval | 0 | 0
Mean | 0
1.97 mN
[1.68, 2.30]
Contact + propagation vs lateral wait
Chart: 
| 1.9485133 | 1.0447813 | 0.61502783 | 0.53543502 | 1.0504259 | 0.64252744 | 1.3842806 | 1.4963941 | 0.62622678 | 1.3289273 | 0.66747288 | 0.93916985 | 0.2647179 | 0.69154342 | 0.086390438 | 1.6913244 | 0.77118216 | 0.42768524 | 0.93269457 | 0.83501442 | 0.50960028 | 1.2781891 | 0.46591738 | 1.3050223
24 histories | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09 | 0.18 | -0.18 | -0.09 | 0 | 0.09
95% interval | 0 | 0
Mean | 0
0.90 mN
[0.72, 1.08]
Three noise draws average within each history. 2,000 history bootstrap resamples. Pointwise exploratory 95% intervals.
Notes: 每个点是一个完整历史的配对改善，先平均它的三次噪声重复，再在24条历史上bootstrap。横轴第一行和后面三行范围不同。区间是探索性的逐项95%区间，不做普遍保证。接触对照除了接触内容，也使用了更长运动跨度，这一点不能隐藏。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/summary.json
2D/runs/information/channels_contact_20261026/metrics.csv
Plot uses stored per-history paired values and stored confidence limits without recomputing selection.

## Slide 15
Appendix: physical checks and reproducibility
15
Item | Recorded status
Material and geometry | 40 x 20 mm body, 10 mm thickness, 576 triangles, dt = 0.01 s
Synthetic relaxation model | E = 20 / 40 / 60 kPa, Poisson ratio 0.35, relaxation 0.12 / 0.90 s
Nominal sensor noise | Position 0.5 um, velocity 0.01 mm/s, force 1.5 mN, lateral 1 um
Physics exceptions | Test penetration 5.030 um and calibration 5.015 um exceed the 5 um limit
Computation and consistency | 0 computation exceptions, 10 regression tests and 7 data checks passed
Notebook and batch runtime | Fresh Docker kernel Run All: 7.61 s. Main batch: 965.85 s on 8 CPU workers
Both penetration overruns remain in the data. Real-material calibration is still missing.
Notes: 数值检查不能只报通过。一条测试历史和一条校准历史的惩罚接触穿透略微超过5微米，已经保留并记录。没有计算异常，通道屏蔽、数据一致性和动作间状态复用检查通过。Notebook在干净Docker内核Run All实测7.61秒，这主要是缓存结果回放，不是重新运行整批实验。主批量生成和评估约16.1分钟。更低的估计误差是同一个模型内部的证据，不代表真实材料已达到亚毫牛精度。
Sources (relative to the repository):
2D/runs/information/channels_contact_20261026/physics.json
2D/runs/information/channels_contact_20261026/failures.json
2D/runs/information/channels_contact_20261026/verification/notebook.json
2D/runs/information/channels_contact_20261026/verification/data_contract.json
2D/runs/information/channels_contact_20261026/RESULTS.md
2D/notebooks/spatial_2d_hidden_state.ipynb

## Slide 16
Questions for discussion
16
Research focus
We want to study hidden state beyond the current observation.
Could too much focus on elasticity shift the project toward soft robotics?
Physical experiment
We can build the model. How should we carry out
these experiments on a real robot?
Broader research question
After studying hidden state through fast and slow forces,
how do we develop the broader idea from this specific case?
Notes: 我想讨论三个问题。第一，我们研究的是当前观测之外的隐藏状态。如果太关注弹性，会不会让研究方向偏向软体机器人？第二，模型可以建立，但真正上实机时，这个实验应该怎么做？第三，我们已经把 hidden state 具体化到快慢力这个点，接下来如何再升华回来，回到更一般的隐藏状态研究问题？
Sources (relative to the repository):
User-provided voice memo: Penn Engineering.m4a (78.396 s). Research focus: 00:00-00:30; real-robot experiments: 00:31-00:46; broader research question: 00:54-01:16. The user confirmed the final word as shenghua (conceptual development).
research/presentations/10.2/assets/question_source.json
These are discussion questions paraphrased from the user-provided memo, not additional experimental findings or attributed adviser instructions.